IDA

Consumer Care Book

Snake, Senseo

Type numbers

Category:	Senseo

Author:	Gérard Verkerk

Date:	2009-03-18

Version:	(PPC)

AKB number:		AKB 32GV-0900001 PPC-Consumer care book Snake

No. of pages:	17

Index

1 Introduction, planning	3

1.1 General Introduction	3

1.2 IPD milestones	6

1.3 Introduction Regions/countries, Quantities, Price	6

1.4 total predictions of sales (sales in Year / total sales)	6

1.5 Consumer Service Offering (CSO) and repair process	7

2 Technical specifications	8

2.1 Range overview	8

2.2 product specifications	8

2.3 New commercial features	8

2.4 Commercial Accessories	10

3 Architecture and characteristics	11

3.1 Mechanical	11

3.2 Electrical	11

3.3 Critical spare parts	12

3.4 Consumer replaceable parts	12

4 Consumer cost of non Quality prediction	12

4.3 FCR (field call rate)	12

4.5 Charge back agreement	13

4.6 Fast feedback program	14

5 consumer care package planning	15

5.1 Consumer care package	15

5.2 special phone number	16

5.3 FAQ (Frequently Asked Questions)	16

Attachment 1: Explanation abbreviations	17

# 1 Introduction, planning

## 1.1 General Introduction

## 1.2 IPD milestones

Project Plan Committed 		PPC: 	wk 913

Concept Consolidation 		CC:	wk 916

Prototype Consolidation	 	PC:	wk 926

Product Validated 		PV:	wk 1015

Industrial Release 		IR:	wk 1023

Commercial Release 		CR: 	wk 1029

## 1.3 Introduction Regions/countries, Quantities, Price

| Type number | FSP | net – net price | Going price |
| --- | --- | --- | --- |
| HD7826 | € 25.69 | € 47.36 | € 89.99 |
| HD7827 | € 29,80 | € 52,63 | € 99.99 |
| HD7835 | € 37,40 | € 71,79 | € 139.99 |

*Not known yet.

## 1.4 total predictions of sales (sales in Year / total sales)

X 1000 units

|  | 2010 | 2011 | 2012 | 2013 |
| --- | --- | --- | --- | --- |
| HD7826 | 510 | 1.020 | 1.104 | 562 |
| HD7827 | 145 | 375 | 404 | 208 |
| HD7835 | 55 | 132 | 143 | 74 |
| Total | 710 | 1.527 | 1.651 | 844 |

## 1.5 Consumer Service Offering (CSO) and repair process

| Region | CSO Front end | CSO Back end | Repair process |
| --- | --- | --- | --- |
| Europe | Call center FAQ Web support FAQ DFU / User manual Leaflet Instruction movies / tutorials Quick start guide | Repair/ carry in | Module swap |

# 2 Technical specifications

## 2.1 Range overview

## 2.2 product specifications

Voltage:			220 - 240V

Power consumption:		1450W

Standby power:			<1W

Frequency:			50-60Hz

etc

## 2.3 New commercial features

Basic features:

- Identical to the Senseo New Generation range

- Using Latte Select podholders

New commercial features:

- New Design

- Higher in cup temperature than Senseo New Generation

- Descaling indicator

- Brewhead lock (identical to Latte Select and Quadrante)

- Real metal finishing for high end models

- Metallic looking finishing for basic end models

- New, innovative materials and finishing

Please also see commercial briefing:

Drinks:

- All SENSEO black coffees

- SENSEO Espresso coffee

- SENSEO Hot Choco

- Pickwick Tea pods

- Ability to vary volume for France (100 ml) and Spain in the future on all models

- Volume variable selection (volume/ strength select feature in high end model) with minimum 80 ml and max 145 ml (France 140 ml)

- Brews 1 or 2 cups at once

For all models MUST

- Standard New Generation (basic end) specifications

- Use existing Latte Select pod holders, only colors may be adapted. The combi podholder Latte Select – New Generation for tea and Hot Choco needs to fit in.

- Perceived compact modernized design is KEY

- Achieve Stiwa “GUT” mark, if necessary through Brew Head Lock (as in Latte Select and Quadrante)

- Standby-losses meeting the regulations sufficiently: stand-by time is 30 minutes and power consumption according to Philips ‘trustful basis’ requirements

- Fitting cups: 100 – 119 mm height adjustment (equal to New Generation)

- The standards, like: pilot light; auto shut-off and minimum water detection

- Water reservoir: minimum new Generation standard 1.2 liter

- Ability to introduce metal lever at higher price points

- Ability to use special finishing such as spray paint and aquadeck such as in SNG Tord Boontje and high end HD7830

- Ability to use new types of materials and finishing (to be proposed by VTA before PPC)

- Meet Green Product requirements (in the most cost effective way)

- Descaling indication

- Have a metal drip tray cover as default

For all models WISH:

- Design:; develop plastic drip-tray cover for low end model, fitting in same housing as metal one.

- Achieve lower than 0.15 Watt off-mode-loss

For higher end models only:

- Volume settings: default mid-point = 122 ml (France 100 ml) and variable selection with minimum 80 ml and max 145 ml (France 140 ml)

- Evolution in user interface vs current New Generation high end model

- Possibly buttons in the top/ integrated with volume select

- Top completely to be made of metal, including handle

- Apply a decorative and functional lighting in such a way it will be perceived as new and innovative by the target group (e.g. high-quality lighting on/around UI or high-quality backlighting in/on cup-area)

Quality and satisfaction

The appliance call rate should not be higher than the objective call rate for Senseo New Generation in 2009 (with all its action points in place)

Consumer satisfaction

Reference for targeted overall satisfaction score is the Senseo New Generation top model

Service requirements should be fully in line with current standard for Senseo. Proposal to be specified by CoC Quality Department.

Launch countries:

- the Netherlands

- Germany, Austria, Switzerland (DACH)

- France

- Belgium

Potential roll-out countries:

- Hungary

- Denmark

- UK

- Spain

## 2.4 Commercial Accessories

Special developed Glasses will be available, Sara Lee activity.

# 3 Architecture and characteristics

## 3.1 Mechanical

(Exploded view / source Senseo NG)

## 3.2 Electrical

(Electrical circuit, source Senseo NG)

## 3.3 Critical spare parts

Consumer replaceable parts + Boiler, 3 way-valve & sealing ring.

## 3.4 Consumer replaceable parts

Podholders, Water tank assy, drip tray cover, drip tray, spout cover & Coffee collector.

# 4 Consumer cost of non Quality prediction

## 4.3 FCR (field call rate)

## 4.5 Charge back agreement

## 4.6 Fast feedback program

| Feedback | regions | Quantity | cost | Yes / No |
| --- | --- | --- | --- | --- |
| Repair via initial workshop? | Europe |  | € 500 | yes |
| Call center feedback | Europe |  | € 5000 | yes |
| Web feedback | Europe |  | € 0 | yes |
| Rapid exchange | Europe | 100 | € 5000 | Yes |
|  |  |  | € |  |

| Total fast feedback cost | € 10500,- |
| --- | --- |

# 5 consumer care package planning

## 5.1 Consumer care package

|  |  | Europe |  |
| --- | --- | --- | --- |
| In-box |  |  |  |
|  | User Manual | Yes | ARC |
|  | Quick Start Guide | Yes | ARC |
|  | Consumer Care Leaflet** | yes | DFU |
| Web |  |  |  |
|  | Warranty Policy Statement (.wbo) |  |  |
|  | Leaflet and Photo's | Yes | DFU/ARC |
|  | FAQ's | Yes | ARC |
|  | Tips and Tricks | Yes | ARC |
|  | Instruction movies (tutorials) | yes | Marcom |
|  | Application Software + read-me file | n.a. | n.a/R&D |
|  | Firmware Upgrade + read-me file | n.a. | n.a/R&D |
|  | On-line connectivity guide | n.a. |  |
|  | Code finder universal remotes | n.a. | n.a/R&D |
| Call Center |  |  |  |
|  | Callcenter Scripts and Tips | Yes | CCQ/ARC |
|  | Training package - technical and soft skills | Yes | CCQ/ARC |
|  | Training execution | Yes | CCQ/ARC |
|  | Product samples | Yes | CCQ/ARC |
| Repair & Exchange |  |  |  |
|  | Service Manual | Yes | CCQ |
|  | Diagnostics- and Service Tools | n.a. | CCQ |
|  | Service Bill of Material, incl. spare parts Purchasing Master data | Yes | CCQ |
|  | Training package diagnostics & repair | n.a. | CCQ |

## 5.2 special phone number

For Europe, Nafta, Latam, Apmea; 800-number will not be added to user manual and quick start guide.

## 5.3 FAQ (Frequently Asked Questions)

FAQ will be translated in to following languages.

- English, Simplified Chinese, French (Belgian French and France French), Dutch, German,

- In a second stage for the countries UK, Hungary, Spain and Denmark

## Attachment 1: Explanation abbreviations

VPD:	Value Proposition Debriefing

AA:	Assignment Agreed

PPC:	Project Plan Committed

CC:	Concept Consolidation

PC:	Prototype Consolidation

PV:	Product Validated

IR:	Industrial Release

CR:	Commercial Release

PE:	Project end

FSP:	Factory Standard Price

IIP:	Internal Invoice Price (FSP + NSO cost)

DFU:	Direction For Use

FAQ:	Fast Ask Questions

CSO:	Consumer Service Offering

ConQ:	Cost of non Quality

ACR:	Average contact Rate

FCR:	Field Call Rate

LATAM 	= Latin America

Nafta		= North America, Canada and Mexico

APMEA		= Asian Pacific, Middle East, Africa

Europe		= Europe

# Text boxes

CMM: Martha Westpalm van Hoorn

(Please place a scan signature)

Date: 2009-03-25

IR

AA

PPC

PV

CR

PE

VPD

IR

PC

CC

CONFIDENTIAL

CONFIDENTIAL